## Slide 1: Optimal Bass Playback in Small Rooms
By Earl Geddes

## Slide 2: The Goal
Everyone wants “great bass”
Toole says its about 20% of our judgment
And yet, poor bass is all too common, if not just plain “typical”
That’s because it’s usually a small room and small rooms are terrible places for “good bass”, at least as I define it
Which begs the question: How do you define “good bass”

## Slide 3: Good Bass
Good bass, in the context of this report, and my personal preference, is a frequency response that has a subtle rise to the lowest frequencies, but which is otherwise very smooth in both frequency and space
Why the “subtle rise”? Why not just flat?
The reason is that the bass in small rooms is always “dead” when compared o larger spaces
Hence a flat response will sound lacking in bass because there is a tradeoff between the sensation of level and the duration of a signal – the shorter signal will sound softer
How much “bass enhancement”?

## Slide 4: How much bass enhancement
I have found that between 3 and 6 dB of bass boost from about 200 Hz down to about 20 Hz is what I judge to be “neutral”
There are those who judge bass by its level despite the fact that this level is not at all natural or neutral
This is not what this discussion is about
This discussion is about “neutral, but adequate bass reproduction in a small room”
I won’t deal with the “Mega Bass” issue

## Slide 5: The small room problem
The small room at low frequencies is “modal”
It is not 2 Pi or 4 Pi or a corner load
  unfortunately those beliefs are all too common resulting in concepts like “room gain” and the like which do not exist in reality for the most part
  A small automobile being just about the only exception that I know of
Modes are interactions of waves traveling in multiple directions creating patterns that are a combination of a stationary pattern and a moving one

## Slide 6: Room modes
The modal region of a room is quite distinct and different from the modeless region above about 100-200 Hz
  I say “modeless” because there are in fact so many modes that individual modes disappear and the room acts like a continuum with no discrete modes
In this modal domain, the only thing that we can talk about is the steady state
The reason for this is simple, it has to do with the detection time of the ear and the reflection times of the room.

## Slide 7: Why steady state?
A 100 Hz tone has a period of 10 ms.
It takes several periods of a sound for the ear to recognize “pitch”
Hence, at 100 Hz the ear has not detected and registered the tone until about 30 ms.
In a small room this wave will have traveled around the room and impinged itself on the listener about a dozen times, each arrival being from a different direction and at a different arrival time.

## Slide 8: Arrival times
While the ear can detect arrival times as short as a few ms at higher frequencies it is simply incapable of doing an assessment of independent arrivals of waves in the modal domain
Hence, at modal frequencies, steady state responses of small rooms is all that we can consider as no temporal aspects of the room are detectable at these frequencies
This whole discussion is quite consistent with the time-frequency tradeoff in measurements, where we simply cannot “window out” the room below some frequency given by the first reflection. This requirement is too stringent for our hearing, but the limitations are quite similar.

## Slide 9: So steady state it is!
There is one caveat to the above discussion – we can detect the “decay” of the steady state response, but this is a much longer time constant than wave-front arrivals.
However, the decay time is almost completely correlated with the modal response
  A “loud” mode tends to decay slower than a “soft” one because a loud mode most likely has low damping while a soft mode most likely has higher damping
Hence, the steady state frequency response of a small room at low frequencies is just about all there is too look at in the modal domain

## Slide 10: Result from PhD thesis
In 1980, my PhD thesis was on the sound field in a small room in the modal domain
This work has been the foundation of all of my thinking about small room bass ever since
This work involved analyzing several rooms of different shapes
In order to compare rooms, I used a metric that averaged the sound field around the room as sources were moved in location as well
This yielded data which showed the best results that a given room could ever achieve

## Slide 11: Results con’t
The best that a room can do is important because it is that aspect of the problem that is the rooms contribution for which no acoustical corrections could be made
  The rooms response could always be worse than these curves, but never better
A few factors stood out as dominate
  The size of the room – bigger is always better
  The damping of the room – more damping is always better
  The rooms shape, but only as it contributes to the damping being seen uniformly by all of the modes

## Slide 12: Results con’t
Interesting, for a room with well distributed damping, the shape was hardly a factor at all
The bottom line then is that for a given room, assuming a fixed size and amount of damping, there is really little to nothing that can be done acoustically to improve the situation
What was noteworthy is that as one reduces the number of source locations, the spatial variance of the sound field would increase

## Slide 13: Results con’t
This is profoundly important because it means that the only hope that any room has of creating a “good bass” sound field is to use EQ, but for a single source this is guaranteed to make the sound field worse at some point while making it better at others.
For a single LF source, there is no “global” solution for the sound field in a small room
It is also unlikely to have better or worse locations when viewed from a global results perspective

## Slide 14: Results con’t
The conclusions here are obvious:
  Only by using several sources in a room can one reduce the spatial variations of the sound field thus allowing for EQ to be effective at smoothing the frequency response of this field at more than one location
  Damping is always an advantage at LFs – unfortunately it is undesirable at HFs and typical damping is ineffective at LFs
    Only damping designed into the structure will actually have a significant effect in the modal region
    Damping on rigid walls, or “traps” are ineffective and hence not a solution to any of these problems

## Slide 15: Small rooms and bass
Small rooms are just about the worst case for creating a “smooth” response at listening positions
They are anything but flat and this response varies continuously around the room
Examples from MathCAD simulations
  Typical sized home room (20 x 14 x 10)
  Listener near the center of the room
  Sources have response to DC

## Slide 16: One Source Room

## Slide 17: One Source Room
The response is quite poor and typical of a small room
The rise to DC is fictitious in real rooms as they are too leaky
Notice that there is no “room gain” as is talked about regularly at various venues
This response could be EQ’d, but only at a single point and it is guaranteed that the response would get worse at other points

## Slide 18: Two Sources

## Slide 19: Two Sources
The first source was in a front corner
The second source was added at the opposite end of the room
The frequency response here is not significantly better, maybe even worse
Lets add a third sub at the side of the room

## Slide 20: Three Source

## Slide 21: Adding Sources
Three sources hardly even changes the results
Adding sources does not necessarily make the frequency response better if we do nothing more than just place them in the room, but
We know that adding more sources does lower the variation of the response around the room by averaging over the modes.
Note what happens when the phase of one source is reversed

## Slide 22: Reverse phase of one source

## Slide 23: The point of multiple subs
The point here is not that reversing the phase of one sub is better or worse
The point is that with multiple subs the interactions between the sources have significant effects on the results
This is not true with the use of just one sub
Also remember that when we have multiple subs, we know that the variations of the response in space will be lower than with just one

## Slide 24: The main point
This raises the idea that if we could somehow manipulate the three subs in an arbitrary (well at least some predictable) way then it has to be possible to optimize the response
And given that there are multiple subs, we know that if we optimize their response that this optimization will hold to a much greater extent around the room than any single sub could ever do

## Slide 25: Gain only

## Slide 26: The Geddes Approach
Use multiple subs
Put one in a front corner
Put one in the back of the room
Put one along one side (if possible)
Take measurements (Holm Impulse)
Optimize the parameters in software (proprietary)
Use results in a DCX2496
Enjoy

## Slide 27: Unfiltered responses

## Slide 28: Filter responses

## Slide 29: Example using DCX2496

## Slide 30: Conclusion
No longer is one at the mercy of the room in achieving ideal audio reproduction down into the modal region of the room
With easy (and free) measurements, some software and readily available DSP, results unobtainable before can be achieved at virtually all listening locations in the room
When one knows that they will be using subs in all cases, then it makes no sense to try and extend the response of the mains